## Slide 1
SAMSUNG INNOVATION CAMPUS · AI CAPSTONE PROJECT
A Two-Stage Deep Learning
Approach to Brain Tumor
Classification & Segmentation
in 2D MRI Images
Pi24, Team 24
Haya Saleh Algarni · Maram Alraddadi · Muslim Alhammad · Raed Almjally
Non-diagnostic · Educational Decision-Support Prototype
Simulated MRI · Illustrative, not a real scan
Notes: Good [morning/afternoon]. We're Pi24, Team 24, and this is our Samsung Innovation Campus AI capstone project: a two-stage deep learning system for brain tumor classification and segmentation in 2D MRI images. Quick introductions of the team, then let's get into it.

## Slide 2
Agenda
1. Foundations
1.1 Problem & Background
1.2 Why AI for Brain MRI?
1.3 Motivation & Objective
1.4 Proposed Solution
1.5 Two-Stage Pipeline Explained
2. Data
2.1 BRISC2025 Dataset
2.2 Dataset Distribution
2.3 Data Preparation & Preprocessing
2.4 Data Augmentation
3. AI Models
3.1 AI Models Overview
3.2 EfficientNet-B0 — Classification
3.3 Custom CNN — Classification
3.4 U-Net + ResNet34 — Segmentation
3.5 Model Comparison & Selection
4. System & Evaluation
4.1 System Workflow & Architecture
4.2 Evaluation Methodology
4.3 Expected Results (Targets)
5. Application & Impact
5.1 User Interface & Deployment
5.2 Limitations & Future Work
5.3 Project Impact & Conclusion
5.4 Thank You / Q&A
Pi24, Team 24 · AI Capstone Project
Agenda
Notes: Here's how we'll walk through the project, in five parts. First, the foundations — the problem, why AI helps here, our motivation, and the pipeline we're proposing. Second, the data we're working with. Third, the AI models themselves — we'll go through each one individually, plus how we're comparing them. Fourth, how it all fits together as a system and how we're evaluating it. And finally, the application, its limitations, and what this all means for the project as a whole.

## Slide 3: Problem & Background
1.1
FOUNDATIONS
01
UNIT
Brain tumors are abnormal tissue growths that require timely, accurate assessment.
MRI is widely used to visualize brain structure and tumor regions.
Two things matter most for every scan: the tumor type, and where it is located.
Manual identification and delineation of tumors is time-consuming — this motivates using deep learning to support the analysis.
WHAT is it?
Tumor type
Glioma / Meningioma /
Pituitary / No Tumor
WHERE is it?
Tumor location
Pixel-level region
within the scan
Pi24, Team 24 · AI Capstone Project
Foundations · 01
Notes: Brain tumors need to be assessed quickly and accurately, and MRI is the standard tool doctors use to do that. For any scan, two things matter: what type of tumor is it, and where exactly is it located. Today, identifying the type and manually outlining the tumor region is done by hand, which takes time and depends on an expert being available. That's the gap we're trying to help close with deep learning.

## Slide 4: Why AI for Brain MRI?
1.2
FOUNDATIONS
02
UNIT
Deep learning models learn visual patterns directly from image data, without hand-crafted rules.
A trained model can act as a fast, consistent second reader to support — not replace — manual review.
Combining classification and segmentation in one pipeline mirrors how a reviewer both identifies and localizes a tumor.
Learns from data
Patterns are learned
directly from pixels
Fast & consistent
A repeatable second
read, every time
Type + Location
One pipeline answers
both questions together
Pi24, Team 24 · AI Capstone Project
Foundations · 02
Notes: So why deep learning specifically? A few reasons. These models learn visual patterns straight from the pixels — we don't have to hand-write rules for what a tumor looks like. A trained model can also act as a fast, consistent second reader, which doesn't get tired or distracted the way a person might on their hundredth scan of the day. And because we're combining classification and segmentation in one pipeline, it mirrors how a radiologist actually works — first figuring out what they're looking at, then figuring out exactly where it is.

## Slide 5: Motivation & Objective
1.3
FOUNDATIONS
03
UNIT
Our motivation: our team set out to build a simple, understandable AI pipeline that pairs tumor-type classification with tumor localization.
BRISC2025 was chosen because it supports both tasks — classification and pixel-level segmentation — from one source.
Our objective: given one T1-weighted axial 2D MRI image, predict one of four classes, and if a tumor is found, produce a tumor mask.
“A non-diagnostic, educational decision-support prototype —
presented through a Gradio interface, not a replacement for a doctor.”
Pi24, Team 24 · AI Capstone Project
Foundations · 03
Notes: Our motivation was to keep this simple and understandable: one pipeline that both classifies the tumor type and localizes it. We picked the BRISC2025 dataset specifically because it gives us both labels and segmentation masks from a single, consistent source. Our objective: take one T1-weighted axial MRI image, predict one of four classes, and when a tumor is present, produce a mask. And to be clear up front — this is an educational, non-diagnostic prototype, not something meant to replace a doctor.

## Slide 6: Proposed Solution
1.4
FOUNDATIONS
04
UNIT
Our proposed solution is a two-stage cascaded pipeline: classify first, then segment only when a tumor is present.
Stage 1 — Classification sorts the image into glioma, meningioma, pituitary tumor, or no tumor.
Stage 2 — Segmentation runs only for tumor-positive images, to localize the tumor region.
Stage 1
Classify
What type of tumor,
if any, is present?
Stage 2
Segment
Where exactly is
the tumor located?
Segmentation is skipped entirely for the “no tumor” class.
Pi24, Team 24 · AI Capstone Project
Foundations · 04
Notes: Here's the core idea at a high level. Stage one classifies the image into glioma, meningioma, pituitary tumor, or no tumor. Stage two only runs if a tumor was detected, and it segments exactly where the tumor is. We deliberately skip segmentation entirely for the no-tumor class — partly because it's unnecessary, and partly because our segmentation model is only trained on tumor-bearing images, so running it on a healthy scan wouldn't mean anything.

## Slide 7: Two-Stage Pipeline Explained
1.5
FOUNDATIONS
05
UNIT
Here is exactly how one MRI image moves through our two-stage pipeline.
MRI Image
Classification
No Tumor
Stop
(report class only)
Tumor Detected
Segmentation
Tumor Mask
Pi24, Team 24 · AI Capstone Project
Foundations · 05
Notes: Let's walk through exactly what happens to one image. It comes in, gets classified first. If the model says no tumor, we stop right there — that's the final answer. If it says tumor detected, that same image gets passed on to our segmentation stage, which outputs a tumor mask showing where the tumor actually is. So classification acts as a gate: segmentation only ever runs when there's something to segment.

## Slide 8: The BRISC2025 Dataset
2.1
DATA
06
UNIT
BRISC2025 (Kaggle): built specifically to support both tumor classification and tumor segmentation from one consistent source.
Provides four diagnostic categories — glioma, meningioma, pituitary tumor, no tumor — each tumor-bearing scan paired with a pixel-level mask.
Current scope: T1-weighted axial 2D MRI images. Coronal and sagittal planes are reserved for future work.
15,586
Total manifest
files
6,000
Classification
images
4,793
Segmentation images
(each with 1 mask)
Pi24, Team 24 · AI Capstone Project
Data · 06
Notes: We're using BRISC2025 from Kaggle, and for this phase of the project we're scoped to T1-weighted axial images only — coronal and sagittal views are a possible future extension. The dataset overall has just over fifteen thousand five hundred files in its manifest. Of that, six thousand images make up our classification set, and about forty-eight hundred tumor-bearing images make up our segmentation set, each with its own pixel-level mask.

## Slide 9: Dataset Distribution
2.2
DATA
07
UNIT
Classification set: 6,000 images (5,000 train / 1,000 test) across four classes.
Glioma
1,147 train
254 test
Meningioma
1,329 train
306 test
Pituitary
1,457 train
300 test
No Tumor
1,067 train
140 test
No Tumor is the smallest class: 21.3% of training data, 14.0% of test data — why macro-F1 and per-class recall matter.
Pi24, Team 24 · AI Capstone Project
Data · 07
Notes: Breaking the classification set down by class: five thousand images for training, one thousand held out for testing, split across our four categories as shown here. One thing worth flagging — No Tumor is our smallest class, at about twenty-one percent of training data and fourteen percent of test data. That's exactly why we're not just tracking overall accuracy — macro-F1 and per-class recall matter here so we don't overlook the minority class.

## Slide 10: Data Preparation & Preprocessing
2.3
DATA
08
UNIT
All data is loaded from a single manifest (path, class, plane, split, mask link) for consistency.
A stratified 15% validation split is carved from the training data, using a fixed random seed shared across the team.
Classification inputs: 224×224 px. Segmentation inputs: 256×256 px. Pixels normalized to the pretrained backbone's expected scale.
Partition
(stratified 15% val)
Pad &
Resize
Normalize
(backbone stats)
Images are padded to a square before resizing, to preserve anatomical proportions across the dataset's non-uniform image sizes.
Pi24, Team 24 · AI Capstone Project
Data · 08
Notes: Everything starts from one manifest file, so class labels, imaging plane, and mask links all come from a single source of truth. From the training data, we carve out a stratified fifteen percent validation split, using a fixed random seed so it's reproducible across the team. We pad every image to a square before resizing, so we don't distort anatomy given the dataset's non-uniform image sizes. Classification images go to 224 by 224, segmentation images to 256 by 256, and pixel values are normalized to match what our pretrained backbones expect.

## Slide 11: Data Augmentation
2.4
DATA
09
UNIT
Applied to the training partition only — validation and test data stay unmodified.
Implemented with Albumentations, which applies identical geometric transforms to each image and its mask together.
Flips
Horizontal &
vertical
Rotation
Limited range
(orientation matters)
Brightness /
Contrast
Scanner robustness
Elastic
Deformation
Anatomical variation
Pi24, Team 24 · AI Capstone Project
Data · 09
Notes: Augmentation is applied only to the training data — validation and test stay untouched, so our evaluation numbers stay honest. We use horizontal and vertical flips, rotation within a limited range since orientation still carries some diagnostic meaning, brightness and contrast adjustment for robustness to different scanners, and elastic deformation to simulate natural anatomical variation. All of this runs through Albumentations, which is important because it applies the exact same geometric transform to an image and its mask together — they never drift out of alignment.

## Slide 12: AI Models Overview
3.1
AI MODELS
10
UNIT
Our team built and compared two classification approaches, plus one segmentation model.
CLASSIFICATION
EfficientNet-B0
Pretrained CNN — Transfer Learning
4-class output
Loss: cross-entropy (class-weighted)
Selection: validation macro-F1
Custom CNN
Built by our team — experimental / comparison model
4-class output
Same training/evaluation protocol
Benchmarked against EfficientNet-B0
VS
SEGMENTATION
U-Net
Pretrained encoder (ResNet34) — Segmentation architecture
Encoder-decoder with skip connections · Loss: Dice + Focal loss · Selection: validation Dice Coefficient
Pi24, Team 24 · AI Capstone Project
AI Models · 10
Notes: On the modeling side, our team built and compared two different approaches for classification, plus one model for segmentation. For classification: EfficientNet-B0, a pretrained CNN we're using through transfer learning, and a custom CNN that we designed and built ourselves as a comparison baseline. For segmentation: U-Net with a pretrained ResNet34 encoder. Let's go through each of these one at a time.

## Slide 13: EfficientNet-B0 — Classification
3.2
AI MODELS
11
UNIT
A pretrained CNN, adapted through transfer learning for our four-class problem.
Original output layer replaced with a 4-unit classification head (glioma, meningioma, pituitary, no tumor).
Cross-entropy loss (mildly class-weighted); best checkpoint chosen by validation macro-F1.
Phase 1
Freeze backbone,
train new head
Phase 2
Unfreeze, fine-tune
end-to-end (lower LR)
Two-phase training protects the pretrained representations from being overwritten by early, noisy gradients.
Pi24, Team 24 · AI Capstone Project
AI Models · 11
Notes: EfficientNet-B0 is a pretrained CNN that we've adapted for our four-class problem through transfer learning. We replaced its original output layer with a four-unit head for glioma, meningioma, pituitary, and no tumor. Training happens in two phases: first we freeze the pretrained backbone and only train the new head, then we unfreeze everything and fine-tune end-to-end at a lower learning rate. That two-phase approach protects the pretrained representations from being overwritten by early, noisy gradients. We use cross-entropy loss, mildly class-weighted, and pick the best checkpoint by validation macro-F1.

## Slide 14: Custom CNN — Classification
3.3
AI MODELS
12
UNIT
An experimental classification model designed and built by our team, used as a comparison point.
Trained and evaluated under the same protocol as EfficientNet-B0, on the same classification data splits.
Purpose: test whether a custom architecture can compete with a transfer-learning approach on this task.
Built in-house
No pretrained weights
Same protocol
Same data, loss & metrics
Comparison model
Benchmarked vs.
EfficientNet-B0
Architecture specifics are still being finalized by the team; results will be reported once training and evaluation are complete.
Pi24, Team 24 · AI Capstone Project
AI Models · 12
Notes: Alongside EfficientNet-B0, we also built our own CNN from scratch, with no pretrained weights, as an experimental comparison model. It's trained and evaluated under exactly the same protocol as EfficientNet-B0 — same data splits, same metrics — so the comparison is fair. The point of this model is really a question: can a custom architecture, built in-house, compete with a transfer-learning approach on this specific task? We're being upfront that the architecture details are still being finalized by the team, and we'll report results once training and evaluation are complete.

## Slide 15: U-Net + ResNet34 — Segmentation
3.4
AI MODELS
13
UNIT
Encoder-decoder segmentation architecture with a pretrained ResNet34 encoder.
Skip connections carry fine spatial detail from encoder to decoder, so tumor boundaries aren't lost to compression.
Loss: Dice + Focal (built for the small tumor-region-to-background imbalance); selection by validation Dice.
Encoder
(ResNet34)
Decoder +
Skip Conn.
Tumor Mask
MRI + predicted tumor mask overlay — the segmentation output.
Pi24, Team 24 · AI Capstone Project
AI Models · 13
Notes: For segmentation we use U-Net, an encoder-decoder architecture, with a pretrained ResNet34 as the encoder. The encoder compresses the image down to figure out what's present, the decoder expands it back up to figure out where, and skip connections carry fine spatial detail across that compression so tumor boundaries don't get lost. Because tumor regions are usually a small fraction of the whole image, we use a combined Dice and Focal loss to handle that imbalance, and we select the best checkpoint by validation Dice score.

## Slide 16: Model Comparison & Selection
3.5
AI MODELS
14
UNIT
We compare EfficientNet-B0 and our custom CNN on methodology — not yet on measured results.
Dimension
EfficientNet-B0
Custom CNN
Starting point
Pretrained on a large image corpus
Trained from scratch by our team
Training approach
Two-phase freeze → fine-tune
Same protocol, end-to-end
Evaluation
Classification test set (1,000 imgs)
Classification test set (1,000 imgs)
Role in final pipeline
Candidate
Candidate
The classification model with the best validated performance (macro-F1) will be selected for the final pipeline.
Pi24, Team 24 · AI Capstone Project
AI Models · 14
Notes: Since we have two classification models, here's how we're comparing them — and I want to be clear this is a methodology comparison, not a results comparison yet. EfficientNet-B0 starts from pretrained weights; our custom CNN starts from scratch. Both go through training, both get evaluated on the exact same thousand-image classification test set with the exact same metrics. Whichever model comes out ahead on validation macro-F1 is the one that gets selected for our final deployed pipeline.

## Slide 17: System Workflow & Architecture
4.1
SYSTEM & EVALUATION
15
UNIT
Our selected classifier and U-Net are combined into a single cascaded pipeline.
Classification uses the best of EfficientNet-B0 or our custom CNN; the interface returns a class prediction and, for tumor cases, a mask overlay — via Gradio.
MRI Input
Classification
(best of EfficientNet-B0 / custom CNN)
Tumor?
No
Final Classification
(no tumor)
Yes
U-Net Segmentation
(ResNet34 encoder)
Tumor Mask Overlay
Gradio Interface (hosted on Hugging Face)
Pi24, Team 24 · AI Capstone Project
System & Evaluation · 15
Notes: Putting it all together: an MRI image comes in, and whichever classification model wins our comparison — EfficientNet-B0 or our custom CNN — classifies it first. If it's predicted as no tumor, we stop there and return that classification. If a tumor is predicted, the same image gets passed to U-Net, which generates a tumor mask, overlays it on the original image, and the whole thing gets served through a Gradio interface hosted on Hugging Face.

## Slide 18: Evaluation Methodology
4.2
SYSTEM & EVALUATION
16
UNIT
Classification and segmentation are evaluated on their own separate held-out test sets — not one shared partition.
Classification Metrics
1,000-image classification test set
Applied identically to EfficientNet-B0 & Custom CNN
Accuracy, per-class precision & recall
Macro-F1, confusion matrix, calibration (ECE)
Segmentation Metrics
860-image segmentation test set
Applied to U-Net
Dice Coefficient and IoU
Precision, recall, per-image distribution
Current evaluation focuses on T1-weighted axial MRI images. Coronal and sagittal planes are reserved for future work.
Pi24, Team 24 · AI Capstone Project
System & Evaluation · 16
Notes: I want to be precise here: classification and segmentation are evaluated on their own separate held-out test sets, not one shared partition. Our two classification models are evaluated identically on the thousand-image classification test set — accuracy, per-class precision and recall, macro-F1, a confusion matrix, and a calibration check. U-Net is evaluated separately on the eight-hundred-sixty-image segmentation test set, using Dice, IoU, precision and recall. And to reiterate our scope: this evaluation is for T1-weighted axial images only, with coronal and sagittal reserved for future work.

## Slide 19: Expected Results (Project Targets)
4.3
SYSTEM & EVALUATION
17
UNIT
The figures below are our project's performance targets — not final test results. They will be verified on the held-out test partitions once training and evaluation are complete.
≥ 0.95
Classification
Macro-F1 (target)
≥ 95%
Overall Accuracy
(target)
≥ 0.90
Per-class Recall
(target, each class)
≥ 0.80
Segmentation
Dice Coefficient (target)
≥ 0.70
Segmentation
IoU (target)
Classification targets apply to whichever model — EfficientNet-B0 or our custom CNN — performs best in our comparison.
Pi24, Team 24 · AI Capstone Project
System & Evaluation · 17
Notes: I want to be upfront: these are our project targets, not final results yet — we haven't completed training and testing, so these numbers describe what we're aiming for, not what we've already achieved. On the classification side, these targets apply to whichever model comes out ahead in our EfficientNet-B0 versus custom CNN comparison. We're targeting macro-F1 of at least 0.95 and overall accuracy of at least 95%, with no single class falling below 90% recall. For segmentation, we're targeting a Dice score of at least 0.80 and an IoU of at least 0.70.

## Slide 20: User Interface & Deployment
5.1
APPLICATION & IMPACT
18
UNIT
Our final prototype will be deployed through a Gradio interface hosted on Hugging Face.
A user will upload a single MRI scan and receive the predicted class with its confidence values.
If a tumor class is predicted, the interface will overlay the tumor-region mask on the original image.
Upload MRI
Gradio App
Prediction +
mask (if tumor)
Hosted on
Hugging Face
Presented explicitly as a decision-support / educational demonstration — not a diagnostic tool.
Pi24, Team 24 · AI Capstone Project
Application & Impact · 18
Notes: On the user side, this will be simple: someone uploads a single MRI scan to our Gradio app. The system will return the predicted class along with confidence values, and if a tumor is predicted, it will also show the mask overlaid on the original scan. Our final prototype will be deployed through Gradio, hosted on Hugging Face, and we'll be explicit in the interface itself that this is a decision-support and educational tool, not something meant for clinical diagnosis.

## Slide 21: Limitations & Future Improvements
5.2
APPLICATION & IMPACT
19
UNIT
We state our limitations in advance, together with the corresponding future work.
Limitations
No patient ID — patient-level split not possible; residual leakage cannot be excluded
All evaluation is retrospective, on one curated dataset
Clinical use would need independent prospective validation + regulatory approval
Future Improvements
Extend to coronal and sagittal image planes
Independent, prospectively collected validation data
Broader robustness testing across scanners/sites
Pi24, Team 24 · AI Capstone Project
Application & Impact · 19
Notes: Two limitations we want to be upfront about. First, the dataset gives us no patient identifier, so we can't guarantee a clean patient-level split — there's a chance of residual data leakage between train and test. Second, everything here is retrospective, tested on one curated dataset; real clinical use would require independent, prospective validation and regulatory approval. Looking ahead, we'd like to extend this to coronal and sagittal planes and test more broadly across different scanners and sites.

## Slide 22: Project Impact & Conclusion
5.3
APPLICATION & IMPACT
20
UNIT
Our project combines tumor-type classification with tumor localization in a single pipeline.
Intended benefit: less time spent on manual tumor delineation, plus a consistent second reading to support expert review.
Presented as a non-diagnostic, educational decision-support system — not a replacement for expert review.
Our two-stage pipeline is designed
to answer both what the tumor is
and where it is — supporting, not
replacing, expert review.
Pi24, Team 24 · AI Capstone Project
Application & Impact · 20
Notes: To sum up: our project brings together tumor-type classification and tumor localization in one pipeline. The intended benefit is cutting down the time spent on manual tumor delineation and giving a consistent second opinion to support review — not replace it. And I want to be clear one more time: this is presented as a non-diagnostic, educational decision-support system. In short, our team built a simple two-stage system that's designed to answer both what the tumor is and where it is.

## Slide 23
THANK YOU FOR YOUR ATTENTION
Questions & Answers
Pi24, Team 24
Haya Saleh Algarni · Maram Alraddadi · Muslim Alhammad · Raed Almjally
A Two-Stage Deep Learning Approach to Brain Tumor Classification & Segmentation in 2D MRI Images
Samsung Innovation Campus · AI Course
Pi24 · Brain Tumor Capstone
Notes: Thank you for your time — we're happy to take any questions.